## Slide 1: Dark Current and Radiation Shielding Studies for the ILC Main Linac
N. Mokhov, I. Rakhno, N. Solyak, A. Sukhanov and I. Tropin
SATIF-13
October 10-12, 2016

## Slide 2: Outline
Introduction
Field Emission and Particle Tracking in SRF
MARS Model
Normal Operation: Radiation in Components and Tunnel
Commissioning Mode: Radiation Loads on Components and Service Tunnel Shielding
Conclusions

## Slide 3: Introduction
Dark current (DC) particles in SRF linac produce radiation affecting
  beam line components and cables inside cryo-module (CM)
  electronics outside of CM in the linac tunnel
  electronics and personnel in the service part of the linac tunnel
Extensive investigation of DC radiation is required during the design of SRF linac
  protect accelerator components from radiation damage
  optimize thickness and cost of radiation shielding
Run MARS15 for the worst case DC model

## Slide 4: Design of ILC Kamaboko Tunnel
Thickness of the wall (1.5-3.5 m)
separating service and operational
parts of the tunnel is determined
by the maximum beam losses.
Reduction of the wall thickness is
a cost effective solution
In the current design, there is a 3.5m wall between main and service tunnels
Change request: Reduce wall thickness (cost saving)

## Slide 5
Eacc = 31.5 MV/m,
DF: 1ms x 10 Hz = 1%
38-m RF unit (period):
4 CM, 26 1.3-GHz cavities,
focusing quad
38m ×40 units = 1.5 km
A detailed modeling is performed for the dark current electrons which are emitted from the surface of the RF cavities and can be repeatedly accelerated in the high-gradient fields in many RF cavities.

## Slide 7: ILC MARS15 Model
Advanced MAD-MARS Beamline
Builder that generates 3D ROOT
geometry for appropriate linac
sections; high-order Runge-Kutta
stepper; energy thresholds
0.001 eV (n) to 100 keV;
start from pre-generated 3D DC
distribution.
Tunnel-x-section
Cryo-module
SRF cavity
Quadrupole magnet

## Slide 8: Modes of Operation
Normal mode, with quadrupole magnets turned ON
Commissioning mode, with quadrupole magnets turned OFF, four scenarios:
  Straight section of the linac (bunch compressor) with steering & correcting magnets turned OFF
  Curved section, which follow Earth curvature with steering & correcting magnets OFF
  Curved linac with perfect alignment and steering magnets ON, but correctors OFF
  Curved linac with random misalignment and with steering and correcting magnets ON – the worst, used for radiation studies here
Steady state equilibrium DC losses

## Slide 9: Normal Operation Mode
Prompt dose (mSv/hr)
25 mSv/hr after 1.2 m concrete

## Slide 10: Normal Mode: Radiation in Cryomodule
Total prompt dose (a.u.)
e± prompt dose (a.u.)
Neutron flux > 100 keV (a.u.)

## Slide 11: Normal Mode: Radiation in Tunnel
Total prompt dose (mSv/hr)
Photon prompt dose (mSv/hr)
Neutron prompt dose (mSv/hr)
Dose right after quadrupole

## Slide 12: Commissioning Mode (Quads OFF)
Power loss per cryo-module along curved linac:
a source for MARS15 modeling
  Red – steering magnets ON, correctors OFF
  Blue - steering magnets ON, correctors ON
The loss in the plateau region—beyond 800m—is used to build the source for MARS15.
One needs about 700m to reach approx. uniform dose distribution.

## Slide 13: Energy Spectrum of Lost Electrons (per RF Unit)
Black – 1st period,
red – 10th period,
green – 20th period
blue – 24th period
magenta – 30 thru 40th period
Curved linac, steering/correctors ON, Quad OFF

## Slide 14: Energy Spectrum of Propagating DC Electrons
At the end of each RF unit
Black – 1st period,
red – 10th period,
green – 20th period
blue – 24th period
magenta – 30-40th period
Curved linac, steering/correctors ON, Quad OFF

## Slide 15: Commissioning Mode: Radiation in CM
Total prompt dose (mSv/hr)
Total absorbed dose (Gy/yr)

## Slide 16: Commissioning Mode: Radiation in Tunnel
Total prompt dose (mSv/hr)
Photon prompt dose (mSv/hr)
Neutron prompt dose (mSv/hr)
25 mSv/hr after 2.2 m concrete

## Slide 17
A
B
25 μSv/hr
Curved linac with Quads OFF
Total prompt dose (50 nA dark current in each cavity)
Case-A: peak dark current losses after quad; Tmax= 0.8 GeV, (quad at 250GeV) Case-B – 40 RF periods, steady-state, Tmax=19.2 GeV (x 20 vs. Case-A)
Quad @250GeV
Case-A
Case-B
1.2m
~2.2m

## Slide 18: Conclusions
In the worst Case-B scenario (all quads are OFF) with 50 nA dark current in each cavity, the beam losses and radiation levels reach steady-state regime after ~800m.
Case-B energy spectrum of lost particles in steady-state extends up to 19.2 GeV compared to only 0.8 GeV in the nominal Case-A
Radiation levels in Case-B are an order of magnitude higher than in Case-A; the design level of 25 mSv/hr in the service tunnel is reached with 1.2 and 2.2 meter thick concrete walls for Case-A and Case-B, respectively. The major contribution to dose behind the wall is due to neutrons
The current design of the ILC Main Linac tunnel with the concrete wall of 3.5 m provides a large safety margin in protection the personnel and electronics in the service tunnel; consider the wall thickness reduction to 2.5-2.7 meters