## Slide 1: Ionizing Radiation Hazards at SLAC from Optical Laser Light Interacting with Matter
Johannes Bauer, James Liu, Sayed Rokni, Ted Liang*
SLAC National Accelerator Laboratory * also Georgia Institute of Technology
SATIF-13, HZDR, Dresden, Germany, October 10-12, 2016

## Slide 2: Outline
Overview of Laser Experiments at MEC
Solid Targets
  Mechanism for creation of Ionizing Radiation
  RP Model (based on PIC Code EPOCH and FLUKA) and measurements
Gas targets
2

## Slide 3: SLAC and LCLS
LCLS
3
Laser Facility at SLAC National Accelerator Laboratory, part of Linac Coherent Light Source (LCLS), at its Matters in Extreme Conditions instrument (MEC)
MEC
Laser hazards unrelated to X-rays from LCLS

## Slide 4: MEC Instrument
Matter in Extreme Conditions (MEC) = LCLS FEL beam (up to 12 keV X-rays) + Optical Laser Beam
target chamber
optical laser
FEL beam
4
Warm Dense Matter (inside Jupiter)
Hot Dense Matter (inertial confinement at NIF)
Shock Waves (through matter)
Electron Acceleration & X-ray Generation
Proton Acceleration

## Slide 5: MEC Instrument (2)
5

## Slide 6: MEC Laser Parameters
6
    Power:
    4 TW: 150 mJ, 10 Hz 2012 - 2014
    25 TW: 1 J, 5 Hz since 2014
    200 TW: 8 J, 1 shot / 8 min starting 2017
    Pulse Duration: ~40 fs
    Optics: focuses beam to few μm diameter
 Irradiance [W/cm2]
= power per area =
energy
time * area

## Slide 7
Three Types of Experiments
Solid Targets:
  Metals (Au, Cu, Ni, etc.); plastics
  Mainly study of Matter in Extreme Conditions (warm dense matter like in Jupiter, confinement for NIF)
  Also proton acceleration
Liquid (Frozen) Targets
  Stream of Liquid H2, D2, etc., freezes in vacuum
  Main goal ion (proton) acceleration
Gas Targets
  Few mm to tens of cm long gas cells; gas jets
  Mainly electron acceleration with Betatron X-ray generation
Protons to 10s MeV
Photons at 10s of keV
Laser Wakefield Acceleration of electrons to few 100 MeV
Hot electrons to MeV level creating Bremsstrahlung
7

## Slide 8: Ionizing Radiation from Laser on Solid Targets
X ray
Laser
Target
Plasma
e-
e-
ions
Laser creates plasma
Electrons accelerated by strong electric field of laser light  PIC code EPOCH
Hot electron energy distribution described with temperature Th
Bremsstrahlung by interaction with target material  FLUKA
8
I (W/cm2) | Th (MeV)
1x1018 | 0.1
1x1019 | 0.7
1x1020 | 3.0

## Slide 9
Target in center
Targets inside Chamber, Laser Beam
9
Spot size (m)
Intensity (W/m2)
Many small peaks = not so good
Gaussian peak = good beam

## Slide 10
Radiation Monitors around MEC Target Chamber
Ion Chamber photon detectors
Moderated BF3 neutron detectors
Passive dosimeters
10

## Slide 11: Solid Target Dose Rate Measurements
  HPI 6032 ion chamber
  6x1017 W/cm2, 30 mJ, 10 Hz
  Dose rate outside hutch
  100 m Au
  1 mm Cu
11
1x1018 W/cm2
Neutrons vs. photons
Strong correlation, but…
…on different scales neutron ~ 25x less than photons
Up to 2 μSv/h outside hutch

## Slide 12: SLAC Measurements
12
Measurements over years at MEC (SLAC) and at Titan (LLNL)
At various angles, mostly with ~1 inch (2.54 cm) Al as shielding

## Slide 13: Particle-In-Cell Code: EPOCH
13
Particle-in-cell (PIC)
    Simulates Maxwell’s equations: EM fields + charged particles
    Physical particles represented by macro-particles containing many physical particles
Implemented in 2D version of EPOCH
    Step 1: Code moves charged particles in space under influence of EM fields, calculates currents from particle motion
    Step 2: Code determines EM field based on new positions and currents
    Repeated in 0.1 fs steps over time from 0 to 600 fs
    Plot direction and energy of (macro)particles both inside area and those that have left the area
Arber, T. D. et al., Contemporary particle-in-cell approach to laser-plasma modelling, Plasma Phys. Control. Fusion 57, 113001 (2015).
https://cfsa-pmw.warwick.ac.uk/EPOCH/epoch

## Slide 14
Laser direction
Density ramp of pre-plasma
1020 W/cm2
Example of PIC Simulation
14

## Slide 15: Example of PIC Simulation
Laser direction
Density ramp of pre-plasma
1020 W/cm2
Electron density per grid, snapshots every 10 fs
15

## Slide 16: Results from PIC Simulation (1)
16
Sample spectrum of hot electrons
Angular distribution around 0o
Angular distribution around 180o
Cold e-
Hot e-

## Slide 17: Results from PIC Simulation (2)
17
Fraction of laser energy converted to ionizing radiation vs irradiance
Forward-backward hot electron yield vs irradiance
Hot Electron Temperature vs Irradiance
Optimization of parameters for highest dose yield

## Slide 18
Simulation from EPOCH
Laser
Target
Simulation from FLUKA
Energy distribution + Angular distribution + Laser absorption +
Geometry
____________________________
 FLUKA dose yield calculation
EPOCH:
3D geometry in FLUKA
Particle In Cell Code: EPOCH
18

## Slide 19: Example of FLUKA Simulations
19
Taking sum of dose outside target chamber
Backward dose mainly from interaction with target chamber
Forward dose mainly from interaction with target in center

## Slide 20: RP Dose Yield Model & SLAC Measurements
Includes 2.54 cm Al
Measurements at various angles
“Revised Model” is basis to determine controls
20
Publication submitted to Radiation Protection Dosimetry
previous model
0o direction
90o direction
180o direction

## Slide 21
Gas Targets: Experiments
21
Average electron spectrum assumed for 2015 experiment
~1.5% conversion efficiency
1.5 mW at 0.1 Hz
number of electrons / MeV
Measured electron
spectrum
Laser Wakefield Acceleration
 electron acceleration
 Betatron oscillation in electric field  short-pulse X-rays used in experiments (similar to FEL X-rays, weak)

## Slide 22
Gas Targets: Shielding
2015 Experiment: 1 J, 12,000 shots in few weeks
Substantial shielding, but only in forward direction
8 cm tungsten
10 cm lead
22

## Slide 23
Simulations around Target Chamber
50 mrem
20 mrem
2000 mrem
75 mrem
5000 mrem
250 mrem
200 mrem
Outside target chamber measurements (1 m, not at 0°)
total 12 mSv (1200 mrem) total
23

## Slide 24
Simulations and Measurements outside Hutch
24
Goal: 100 μSv (no dosimeters)
Measurements outside hutch
(5 m, 0° behind shielding)
Maximal 84 μSv total

## Slide 25
Conclusion
25
Ionizing Radiation from lasers need to be addressed
Solid Targets
  SLAC developed source term
  Measurements comparing against models
  Latest model based on PIC simulations
Gas Targets
  Source term better known
  Simulations to design shielding
Laser research field is growing

## Slide 26: Thank You!
26