## Slide 1: Measurements and FLUKA Simulations of Bismuth and Aluminum Activation at the CERN Shielding Benchmark Facility(CSBF)
SATIF 13, 12/10/2016
E. Iliopoulou, R. Froeschl, M. Brugger, S. Roesler, A. Infantino, N. Nakao, T. Sanami, T. Kajimoto, A. Siountas, P. Bamidis

## Slide 2: Outline
CHARM (CERN High energy AcceleRator Mixed field facility)
CSBF (CERN Shielding Benchmark Facility)
Activation benchmark campaign in July 2015
FLUKA simulations
Sensitivity studies
Results
Conclusions

## Slide 3: CHARM - Location

## Slide 4: CHARM - Layout
Target
Target alcove
Movable shielding
walls
Beam line

## Slide 5: CHARM
Purpose
  Study radiation effects on electronic components (R2E project)
Beam characteristics
  Primary protons from the PS
  24 GeV/c momentum
  5 x 1011 protons/pulse
  350ms pulse length
  max. average beam intensity 6.6 x 1010 p/s

## Slide 6: CHARM
4 movable shielding walls
Target holder

## Slide 7: CSBF (CERN Shielding Benchmark Facility)
Combined facility EN/EA, R2E and RP
Purpose
  Characterization of the shielding properties of various materials
  Deep shielding penetration studies
    Detector calibration
    Detector inter-comparison
    Activation
Situated laterally above the CHARM target
  Parasitic use of the radiation field emerging from the CHARM target
80cm cast iron & 360cm of concrete and barite concrete

## Slide 8: CSBF – Layout 2015

## Slide 9: CSBF - Location

## Slide 10: Activation benchmark campaign in July 2015
Bismuth & aluminum samples
  11 disk samples
  Different heights in the CSBF
  Inside CHARM
Copper target
Specific production yield comparison
  FLUKA simulations
  Measured activity Production yield

## Slide 11: FLUKA simulations
Protons with 24GeV/c on Cu target
  12mm x 12mm FWHM
Region importance biasing
Usrtrack – scoring for neutron fluence
  Weighting with a set of cross sections of Bi(n,xn) and Al(n,a)Na-24
Correct geometry description
  Scoring volumes

## Slide 12: FLUKA simulations

## Slide 13: FLUKA simulations

## Slide 14: Sensitivity studies
Beam profile on target (FWHM)
  From 12mm x 12mm 36mm x 36mm
  Negligible impact
Material upstream inside IRRAD
  <1% for actual material inside IRRAD
  20% hypothetical difference from loading case for RP design study
Density of materials
  Concrete, from 2.2g/cm3 2.4g/cm3
  Cast Iron, from 7.3g/cm3 7.2g/cm3

## Slide 15: Samples

## Slide 16: Sample placement

## Slide 17: Beam intensity profile

## Slide 18: Results

## Slide 19: Results

## Slide 20: Results

## Slide 21: Conclusions
Activation campaign at CSBF 2015
Comparison of production yields between FLUKA and
γ-spectrometry measurements
Agreement at a level of a factor of 1.5.
Upgrade of CSBF in 2016, see further details in SATIF13 talk:
  R. Froeschl et al: Radiation protection aspects of the commissioning and operation of CERN High energy AcceleRator Mixed field (CHARM) facility in the CERN East Experimental Area

## Slide 22
Thank you for your attention!

## Slide 23
BACKUP

## Slide 24: Upgrade of CSBF
Requirements:
  Passive detectors
    Activation samples or passive dosimeters
    Monte Carlo benchmark studies
  Active detectors
    On top of the shielding
    Deep penetration neutron spectrum
  Dosimeters attached to phantoms
    On top of the shielding
    Deep penetration neutron spectrum
  Shielding material test location
    Measurement of the attenuation length for different materials
Detailed design based on FLUKA simulations

## Slide 25: Upgrade of CSBF –Layout

## Slide 26: Upgrade of CSBF

## Slide 27: Backup - Upgrade

## Slide 28: Backup - Upgrade

## Slide 29: Backup - Upgrade