## Slide 1: Competitive Reaction in Cyclotrons F-18 Production – Regulatory Implications
Accelerators and Class II Facilities Division
Canadian Nuclear Safety Commission
SATIF-13
(October 2016 – Dresden, GE)
Angel Licea, MEng

## Slide 2
Established May 2000 under the Nuclear Safety and Control Act
Replaced the Atomic Energy Control Board, established in 1946 under the Atomic Energy Control Act
Regulate the use of nuclear energy and materials to protect the health, safety and security of Canadians and the environment
Implement Canada's international commitments on the peaceful use of nuclear energy
Disseminate objective scientific, technical and regulatory information to the public
Mandate

## Slide 3: Background -
In the last forty years, positron emission tomography (PET) has advanced rapidly and is becoming an indispensable imaging modality for the evaluation of cancer patients.
Of the hundreds of positron labelled radiotracers, 2-[18F]-fluoro-2-deoxy-D-glucose (FDG) is the most successful and widely used imaging agent in PET today
F-18

## Slide 4
Canada is no exception; last year, a total combined 18F production of 1.37 PBq at the end of bombardment (EOB) was reported from the cyclotron facilities licenced by the CNSC.

## Slide 5
Publications
In 2004 Shileki Ito and al, confirmed the presence of tritium in enriched [18O]water irradiated with 9.6MeV protons used to produce [18F] fluoride via 18O(p, n)18F , reaction was inferred from the cross sections and threshold energies of the reaction..
Tomiyoshi et al., (1999) also detected tritium in [15O]water as a by-product of the 14N(d, t)13N when the 15O was produced by the 14N(d, n)15O reaction with 8.6MeV deuterons.
18 O+p->3H + 16O

## Slide 6
Publications
MiniTrace GE 9.6 MeV protons, 25 µA, 1.38 ml target capacity (self-shielded baby cyclotron)
Beckman LS-6000, scintillation counter

## Slide 7
Distribution of tritium in each step from 18F production to [18F]FDG purification
T - 63.5 kBq
T - 46.1 kBq
T - 43.3 kBq
T - 1.3 kBq
T - 0.726 kBq
T - N.D.
93 % of T is recuperated for recycling
(18F ) 17.4 GBq EOB
(18F ) 8.59 GBq EOS

## Slide 8
Publication..
In 2011, Romolo Remetti et al .. FLUKA simulation and radiometric characterization of proton irradiated [18O]H2O for the treatment of the waste streams originated from [18F]FDG synthesis process
PetTrace GE, 16.5 MeV, 37 µA for an hour in two samples, no synthesis of F-18.
Measured 36 & 33 kBq/ml slightly below than Ito et al.
- 50 kBq/ml simulated with FLUKA,
 | H.L. | A (Bq)
Ni57 | 35.60 h | 188.919
Co58 | 70.86 d | 856.403
Co57 | 271.8 d | 51.88
Mn52 | 5.591 d | 198.997
Mn52 | 5.591 d | 204.346
Mn52 | 5.591 d | 198.58
Co56 | 77.27 d | 430.836
Mn54 | 312.3 d | 5.034
Cr51 | 27.70 d | 807.185
Cd109 | 463.55 d | 246.632
Re183 | 70.02 d | 11.229
Gamma emitters detected in water samples

## Slide 9
Publication…
Cyclone IBA, 18 MeV, 40 µA for an hour in 24 separated runs.
Tritium activity in unirradiated enriched water varies from 1400 to 0.4 Bq/ml.
Mochizuki et al (2006) reported the presence of tritium in non irradiated H218O used to rinse their target vessel at a much greater concentration of 92 kBq/ml.
Measured from 71.3 to 91.8 kBq/ml with a mean of 80.6 kBq/ml, very close to Ito’s results.
In 2014, C Marshall et al, Quantification of the activity of tritium produced during the routine synthesis of 18F[FDG] for positron emission tomography

## Slide 10
The reactions..
https://www-nds.iaea.org/

## Slide 11
Thunder Bay
MNIH
Vancouver
CAMH & UHN
Five Canadian facilities…
Participated for some measurements,
Non-irradiated enriched water
Samples after the EOB
Different cyclotrons
Different conditions
CNSC lab analyzed most of samples*
* A Tri-Carb (low background level) Liquid Scintillation Counter was used to measure the tritium activity

## Slide 12
Sampling results…
a – Two 2.5 ml targets, dual extraction, volumes mixed at the end of the run.
b – Diluted 30%
c – Produced their own analysis of five recovering water samples, no samples of unirradiated water were provided.
Centre | Cyclotron | Energy (MeV) | Current (µA) | Time (min) | Supplier (H218O) | Tritium (kBq/ml)
TBRHSC | TR24 | 18 | 100 | 60 | Rotem | 181.8
 | n/a | n/a | n/a | n/a | Rotem | 0.0004
VCC | TR19 | 19 | 60 | 36 | Huayi | 57.07
 | n/a | n/a | n/a | n/a | Huayi | 5.22
UHN | PETTrace | 16.5 | 48/target | 130/126a | Rotem | 268.7
 | n/a | n/a | n/a | n/a | Rotem | 0.0009
CAMH | IBA Cyclone | 18 | 40 | 30 | Huayi | 70.57
 | n/a | n/a | n/a | n/a | Huayi | 31.74
 | MC-17 | 17 | 40 | 30 | Huayi | 22.32b
MNIHc | IBA Cyclone | 18 | 40 | 60 | Isoflex | 31.65

## Slide 13
UHN – dual irradiation sample (5 ml) to decay below 200 Bq/g (2.2 days for 18F and more than 100 years for Tritium)

## Slide 14
Regulatory issues..
Licensing
In order to license the tritium concentration produced as a competitive reaction in the production of 18F, concentration has to exceed 1 MBq/g (Schedule 1), this is not the case in any Canadian cyclotron normal operation (optimal 18F production is in less than two hours).
Unconditional releases of tritium concentration shall comply with the limits indicated in Schedule 2, which is 200 Bq/g. Then dilution of enriched water wastes is strongly recommended if the licensee choose this option.
Import/Export
tritium concentration in export/import transactions with enriched water shall not exceed the ratio of tritium to hydrogen by atoms 1 part in 1000. This ration is equivalent to 6.023E+19 atoms of tritium per millilitre in enriched water which computes in a tritium activity of 107.2 GBq/ml, again not possible in any Canadian recycling or new stock export/import operation

## Slide 15: Conclusion
Tritium is present in unirradiated enriched water, concentrations may vary from 0.6 Bq to < 100 kBq.
During the production of 18F, tritium is also produced via a competitive reaction and it can be recovered in the enriched water (~ 93%) .
Tritium is not present in the final product FDG.
Some cyclotron licensees recycle the recovered water from the synthesis to the suppliers.
Right now, the enriched water sent for recycling, there is no monitoring for tritium nor when “virgin” enriched water is received by the licensees, more important, there is no indication of tritium concentration in the Certificate of Analysis provided by suppliers of “virgin” stock .
Tritium concentration in 18F production vary from cyclotron, target and materials (target body, havar window, etc), its concentration does not trigger any regulatory consequences other than the unconditional release.
Procedure in place to monitor tritium concentration in new stock and inventory (annual compliance report), inspection sampling, etc.

## Slide 16: Next Steps
Complete the trititum survey of the rest cyclotron production of F-18 (EOB) in Canada.
Work with Heath Canada to include the tritium content in their cGMP Certificate of Analysis.
Implement a procedure to monitor tritium concentration in new stock and operational inventory (annual compliance report).
Share this information to the other international forums.

## Slide 17: Thank you
For more details
http://nuclearsafety.gc.ca/eng/nuclear-substances/licensing-class-II-nuclear-facilities-and-prescribed-equipment/index.cfm#ClassIINuclearFacilities
Email
Angel.Licea@Canada.Ca
Questions?